## Slide 1
Function: func_1
Solve
Input
xdata: ndarray (n x 1)
Output
ndarray (n x 1)
Function: func_2
Solve
Input
xdata: ndarray (n x 1)
Output
ndarray (2 x n x 1)
Function: func_3
Solve
Input
xdata: ndarray (n x 1)
Output
ndarray (3 x n x 1)
Function: func_4
Solve
Input
xdata: ndarray (2 x 1 x n x m)
Output
ndarray (n x m x 2 x 1)
Function: func_5
Solve
Input
xdata: ndarray (2 x 1 x n x m)
Output
ndarray (n x m x 3 x 1)
Function: plotter
Compute injected function and make line or contour plot(s) for resulting ydata
Input
xdata: ndarray of shape…
  (n) – 1D
  (n x 1) – 2D column vector
  (2 x n x m) – 2D grid
Output
Figures
Figure(s)
Start
xdata
function
Functions
xdata
ydata
Invoke function
xdata
ydata

## Slide 2
Function: compute_N
Compute the shape function matrix for a 2D element, one for each point in the input grid of natural coordinates
Input
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x 2 x nnodes*2)
Function: plot_element_shape_functions
Make a grid of plots for individual shape functions for an element
Input
N: ndarray (n x m x 2 x nnodes*2)
grid: ndarray (n x m x 2 x 1)
Output
Figures
Function: make_natural_grid
Make ngrid x ngrid array of coordinates in the natural coordinate system from (-1, 1)
Input
(optional) ngrid: int
Output
ndarray (ngrid x ngrid x 2 x 1)
Function: interpolate
Solve
Input
nodal_vec: ndarray (nnodes*2 x 1)
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x nnodes*2 x 1)
grid in
grid in
ngrid
nodal coords in
Plot in natural coordinate sys
Plot in local element coordinate sys
Figure(s)

## Slide 3
Function: make_natural_grid
Make ngrid x ngrid array of coordinates in the natural coordinate system from (-1, 1)
Input
(optional) ngrid: int
Output
ndarray (ngrid x ngrid x 2 x 1)
Function: interpolate
Solve
Input
nodal_vec: ndarray (nnodes*2 x 1)
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x nnodes*2 x 1)
ngrid
nodal displacements
grid in
Function: interpolate
Solve
Input
nodal_vec: ndarray (nnodes*2 x 1)
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x nnodes*2 x 1)
Function: plot_element_displacement
Make a grid of plots for displacements on the element, one for each component
Input
u: ndarray (n x m x nnodes*2 x 1)
grid: ndarray (n x m x 2 x 1)
Output
Figures
element displacements
grid in
nodal coords in
Plot in natural coordinate sys
Plot in local element coordinate sys
Figure(s)

## Slide 4
compute_strain
Compute the strains for a 2D element.
Input
B: ndarray (n x m x 3 x nnodes*2)
q: ndarray (n x m x nnodes*2 x 1)
Output
ndarray (n x m x 3 x 1)
compute_stress
Compute the strains for a 2D element.
Input
D: ndarray (n x m x 3 x 3)
eps: ndarray (n x m x 3 x 1)
Output
ndarray (n x m x 3 x 1)
make_natural_grid
Make ngrid x ngrid array of coordinates in the natural coordinate system from (-1, 1)
Input
(optional) ngrid: int
Output
ndarray (ngrid x ngrid x 2 x 1)
compute_dN
Compute the shape function derivative matrix for a 2D element, one for each point in the input grid of natural coordinates
Input
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x 4 x nnodes*2)
compute_jacobian
Compute the full Jacobian matrix for a 2D element, one for each point in the input grid of shape function derivative matrices.
Input
dN: ndarray (n x m x 4 x nnodes*2)
Output
ndarray (n x m x 4 x 4)
compute_B_matrix
Compute the matrix for a 2D element, one for each point in the one for each point in the input grid of shape function derivative/full Jacobian matrices.
Input
dN: ndarray (n x m x 4 x nnodes*2)
J: ndarray (n x m x 4 x 4)
Output
ndarray (n x m x 3 x nnodes*2)
ngrid
grid in
compute_D_isotropic_plane_stress
Compute the 2D stiffness matrix for an isotropic material assuming plane stress.
Input
E: float
nu: float
Output
ndarray (3 x 3)
compute_D_isotropic_plane_strain
Compute the 2D stiffness matrix for an isotropic material assuming plane strain.
Input
E: float
nu: float
Output
ndarray (3 x 3)
Element stress
nodal displacements
Isotropic plane strain
Isotropic plane stress
E

## Slide 5
test_2D_shape_functions
Run tests to verify the shape function matrix computations for an instantiated class of base type Element2D.
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
Instance: Element2D base class
ngrid
test_2D_shape_function_derivatives
Run tests to verify the shape function derivative matrix computations for an instantiated class of base type Element2D.
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
test_2D_jacobian
Run tests to verify the full Jacobian matrix computations for an instantiated class of base type Element2D
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
test_2D_B_matrix
Run tests to verify the full matrix computations for an instantiated class of base type Element2D.
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
inspect_2D_element
Given a 2D element, 2D stiffness matrix , and nodal displacements, compute the stresses and strains on the element for a grid of points in both the local element and natural coordinate systems. Generate a collection of contours for the element: 1) shape functions, 2) displacements, 3) Jacobian, 4) stresses and strains
Input
elem: mfe.baseclasses.Element2D
D: ndarray (3 x 3)
q: (nnodes*2 x 1)
(optional) ngrid: int
Output
Figures
compute_D_isotropic_plane_stress
Compute the 2D stiffness matrix for an isotropic material assuming plane stress.
Input
E: float
nu: float
Output
ndarray (3 x 3)
compute_D_isotropic_plane_strain
Compute the 2D stiffness matrix for an isotropic material assuming plane strain.
Input
E: float
nu: float
Output
ndarray (3 x 3)
E
nodal displacements
Figure(s)

## Slide 6
compute_strain_energy_density
Compute the strain energy density for a 2D element.
Input
sigma: ndarray (n x m x 3 x 1)
eps: ndarray (n x m x 3 x 1)
Output
ndarray (n x m x 1 x 1)
compute_k
Compute the stiffness matrix for a 2D element using Gaussian quadrature, where and are evaluated at the element’s integration points .
Input
ip_grid: ndarray (num_pts x num_pts x 2 x 1)
w_ij: ndarray (num_pts x num_pts x 1 x 1)
D: ndarray (3 x 3)
thickness: float
Output
ndarray (n x m x 2*nnodes x 2*nnodes)
Figure
plot_element_strain_energy_density
Plot the strain energy density for a grid of points for a 2D element as a contour.
Input
psi: ndarray (n x m x 1 x 1)
grid: ndarray (n x m x 2 x 1)
Output
Figure
plot_element_stiffness_matrix
Plot the stiffness matrix for a 2D element as a colormap.
Input
D: ndarray (nnodes x nnodes)
Output
Figure
Figure
make_ip_grid
Make a grid of integration points and their weights for performing gaussian quadrature on a 2D element.
Input
num_pts: int
Output
ndarray (num_pts x num_pts x 2 x 1)
ndarray (num_pts x num_pts x 1 x 1)
num_pts

## Slide 8
Compute the value of the shape function for node as a function of position within the element in terms of the natural coordinate system
self.shape_n
Compute the shape function matrix for a 2D element with nodes in terms of the natural coordinate system
self.N
Interpolate the value of quantity as a function of position within the element given a vector of nodal values for a grid of coordinates in the natural coordinate system using shape functions
self.interpolate
Return a list of shape functions for the element ordered by local node number
self.get_shape_funcs
Generic 2D element class
Plot the value of each shape function for the element in either the natural () or local () coordinate systems for a grid of coordinates
plot_shape_functions
: or positions within the element
Figure(s)
or within the element

## Slide 9
Compute the value of the shape function for node as a function of position within the element in terms of the natural coordinate system
self.shape_n
Compute the shape function matrix for a 2D element with nodes in terms of the natural coordinate system
self.N
Interpolate the value of quantity as a function of position within the element given a vector of nodal values for a grid of coordinates in the natural coordinate system using shape functions
self.interpolate
Return a list of shape functions for the element ordered by local node number
self.get_shape_funcs
Generic 2D element class
Plot the value of interpolated quantity within the element in either the natural () or local () coordinate systems for a grid of coordinates given a given a vector of nodal values
plot_element_field
: displacements within the element
: or positions within the element
Figure(s)
or displacements within the element