## Slide 1
func_1
Solve
Input
xdata: ndarray (n x 1)
Output
ndarray (n x 1)
func_2
Solve
Input
xdata: ndarray (n x 1)
Output
ndarray (2 x n x 1)
func_3
Solve
Input
xdata: ndarray (n x 1)
Output
ndarray (3 x n x 1)
func_4
Solve
Input
xdata: ndarray (2 x 1 x n x m)
Output
ndarray (n x m x 2 x 1)
func_5
Solve
Input
xdata: ndarray (2 x 1 x n x m)
Output
ndarray (n x m x 3 x 1)
Callable functions
plotter
Compute injected function and make line or contour plot(s) for resulting ydata
Input
xdata: ndarray (n x 1) or (2 x 1 x n x m)
function: Callable
Output
Figures

## Slide 2
Callable function
plotter
Input
xdata: ndarray (n x 1) or (2 x 1 x n x m)
function: Callable
Output
Figures
Figure(s)
xdata
function callable
xdata
ydata
xdata
ydata

## Slide 3
compute_N
Compute the shape function matrix for a 2D element, one for each point in the input grid of natural coordinates
Input
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x 2 x nnodes*2)
plot_element_shape_functions
Make a grid of plots showing the value of individual shape functions comprising components of the shape function matrix within an element, one per for each unique shape function
Input
N: ndarray (n x m x 2 x nnodes*2)
grid: ndarray (n x m x 2 x 1)
Output
Figures
make_natural_grid
Construct a 2D array of coordinates in the natural coordinate system from (-1, 1) in each orthogonal direction.
Input
(optional) ngrid: int
Output
ndarray (ngrid x ngrid x 2 x 1)
map_to_element
Solve , where is a column vector of some quantity at the element nodes, is the shape function matrix for the element, and are the values of the quantity mapped onto the element
Input
nodal_vec: ndarray (nnodes*2 x 1)
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x nnodes*2 x 1)
plot_element_displacement
Make a grid of plots for displacements on the element, one for each component
Input
u: ndarray (n x m x nnodes*2 x 1)
grid: ndarray (n x m x 2 x 1)
Output
Figures
Key functions
HW2

## Slide 4
ngrid
compute_N
Input
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x 2 x nnodes*2)
make_natural_grid
Input
(optional) ngrid: int
Output
ndarray (ngrid x ngrid x 2 x 1)
plot_element_shape_functions
Input
N: ndarray (n x m x 2 x nnodes*2)
grid: ndarray (n x m x 2 x 1)
Output
Figures
map_to_element
Input
nodal_vec: ndarray (nnodes*2 x 1)
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x nnodes*2 x 1)
Figures
grid
plot_element_displacement
Make a grid of plots for displacements on the element, one for each component
Input
u: ndarray (n x m x nnodes*2 x 1)
grid: ndarray (n x m x 2 x 1)
Output
Figures
Figures
u
grid
Bubble charts
HW2

## Slide 5
Key functions
HW3
compute_stress
Compute the strains for a 2D element.
Input
D: ndarray (n x m x 3 x 3)
eps: ndarray (n x m x 3 x 1)
Output
ndarray (n x m x 3 x 1)
compute_dN
Compute the shape function derivative matrix for a 2D element, one for each point in the input grid of natural coordinates
Input
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x 4 x nnodes*2)
compute_J
Compute the full Jacobian matrix for a 2D element, one for each point in the input grid of shape function derivative matrices.
Input
dN: ndarray (n x m x 4 x nnodes*2)
Output
ndarray (n x m x 4 x 4)
compute_B
Compute the matrix for a 2D element, one for each point in the one for each point in the input grid of shape function derivative/full Jacobian matrices.
Input
dN: ndarray (n x m x 4 x nnodes*2)
J: ndarray (n x m x 4 x 4)
Output
ndarray (n x m x 3 x nnodes*2)
compute_D_isotropic_plane_stress
Compute the 2D stiffness matrix for an isotropic material assuming plane stress.
Input
E: float
nu: float
Output
ndarray (3 x 3)
compute_D_isotropic_plane_strain
Compute the 2D stiffness matrix for an isotropic material assuming plane strain.
Input
E: float
nu: float
Output
ndarray (3 x 3)
compute_strain
Compute the strains for a 2D element.
Input
B: ndarray (n x m x 3 x nnodes*2)
q: ndarray (n x m x nnodes*2 x 1)
Output
ndarray (n x m x 3 x 1)
compute_N
Compute the shape function matrix for a 2D element, one for each point in the input grid of natural coordinates
Input
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x 2 x nnodes*2)

## Slide 6
Key unit test functions
HW3
test_2D_shape_functions
Run tests to verify the shape function matrix computations for an instantiated class of base type Element2D.
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
test_2D_shape_function_derivatives
Run tests to verify the shape function derivative matrix computations for an instantiated class of base type Element2D.
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
test_2D_jacobian
Run tests to verify the full Jacobian matrix computations for an instantiated class of base type Element2D
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
test_2D_B_matrix
Run tests to verify the full matrix computations for an instantiated class of base type Element2D.
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
inspect_2D_element
Given a 2D element, 2D stiffness matrix , and nodal displacements, compute the stresses and strains on the element for a grid of points in both the local element and natural coordinate systems. Generate a collection of contours for the element: 1) shape functions, 2) displacements, 3) Jacobian, 4) stresses and strains
Input
elem: mfe.baseclasses.Element2D
D: ndarray (3 x 3)
q: (nnodes*2 x 1)
(optional) ngrid: int
Output
Figures

## Slide 7
ngrid
make_natural_grid
Input
(optional) ngrid: int
Output
ndarray (ngrid x ngrid x 2 x 1)
Bubble charts: key functions
HW3
compute_dN
Input
natural_grid: ndarray (n x m x 2 x 1)
Output
ndarray (n x m x 4 x nnodes*2)
compute_B
Input
dN: ndarray (n x m x 4 x nnodes*2)
J: ndarray (n x m x 4 x 4)
Output
ndarray (n x m x 3 x nnodes*2)
compute_J
Input
dN: ndarray (n x m x 4 x nnodes*2)
Output
ndarray (n x m x 4 x 4)
compute_strain
Input
B: ndarray (n x m x 3 x nnodes*2)
q: ndarray (n x m x nnodes*2 x 1)
Output
ndarray (n x m x 3 x 1)
compute_stress
Input
D: ndarray (n x m x 3 x 3)
eps: ndarray (n x m x 3 x 1)
Output
ndarray (n x m x 3 x 1)
compute_D_isotropic_plane_stress
Input
E: float
nu: float
Output
ndarray (3 x 3)
compute_D_isotropic_plane_strain
Input
E: float
nu: float
Output
ndarray (3 x 3)
Isotropic plane stress
Isotropic plane strain

## Slide 8
Instance: Element2D class
ngrid
Bubble charts: unit test functions
HW3
compute_D_isotropic_plane_stress
Input
E: float
nu: float
Output
ndarray (3 x 3)
compute_D_isotropic_plane_strain
Input
E: float
nu: float
Output
ndarray (3 x 3)
Isotropic plane stress
Isotropic plane strain
test_2D_shape_functions
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
test_2D_shape_function_derivatives
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
test_2D_jacobian
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
test_2D_B_matrix
Input
elem: mfe.baseclasses.Element2D
(optional) ngrid: int
Output
None
inspect_2D_element
Input
elem: mfe.baseclasses.Element2D
D: ndarray (3 x 3)
q: (nnodes*2 x 1)
(optional) ngrid: int
Output
Figures
Instance: Element2D class
ngrid
Figures

## Slide 9
Key functions
HW4
compute_strain_energy_density
Compute the strain energy density for a 2D element.
Input
sigma: ndarray (n x m x 3 x 1)
eps: ndarray (n x m x 3 x 1)
Output
ndarray (n x m x 1 x 1)
compute_k
Compute the stiffness matrix for a 2D element using Gaussian quadrature, where and are evaluated at the element’s integration points .
Input
ip_grid: ndarray (num_pts x num_pts x 2 x 1)
w_ij: ndarray (num_pts x num_pts x 1 x 1)
D: ndarray (3 x 3)
thickness: float
Output
ndarray (n x m x 2*nnodes x 2*nnodes)
plot_element_strain_energy_density
Plot the strain energy density for a grid of points for a 2D element as a contour.
Input
psi: ndarray (n x m x 1 x 1)
grid: ndarray (n x m x 2 x 1)
Output
Figure
plot_element_stiffness_matrix
Plot the stiffness matrix for a 2D element as a colormap.
Input
D: ndarray (nnodes x nnodes)
Output
Figure
make_ip_grid
Make a grid of integration points and their weights for performing gaussian quadrature on a 2D element.
Input
num_pts: int
Output
ndarray (num_pts x num_pts x 2 x 1)
ndarray (num_pts x num_pts x 1 x 1)

## Slide 10
num_itg_pts
Bubble charts
HW4
compute_strain_energy_density
Input
sigma: ndarray (n x m x 3 x 1)
eps: ndarray (n x m x 3 x 1)
Output
ndarray (n x m x 1 x 1)
compute_k
Input
ip_grid: ndarray (num_pts x num_pts x 2 x 1)
w_ij: ndarray (num_pts x num_pts x 1 x 1)
D: ndarray (3 x 3)
thickness: float
Output
ndarray (n x m x 2*nnodes x 2*nnodes)
plot_element_strain_energy_density
Input
psi: ndarray (n x m x 1 x 1)
grid: ndarray (n x m x 2 x 1)
Output
Figure
plot_element_stiffness_matrix
Input
D: ndarray (nnodes x nnodes)
Output
Figure
make_ip_grid
Input
num_pts: int
Output
ndarray (num_pts x num_pts x 2 x 1)
ndarray (num_pts x num_pts x 1 x 1)
Figures
or
Figures

## Slide 11
Key functions
HW5
compute_fs
Compute surface traction polynomials at all integration points on the surface in the local element coordinate system
Input
funcs: ndarray of Callable (2 x 1)
coeff: ndarray (2 x ncoeff)
grid: ndarray (2 x 1)
Output
ndarray (n x m x 2 x 1)
compute_J_det_surf
Compute the Jacobi-determinant along the traction surface , where if the traction is applied on a face where the component is varied, and where the component is varied.
Input
J: ndarray (n x m x 4 x 4)
grid_shape: ndarray (n x m x 2 x 1)
face: str (+x, -x, +y, -y)
Output
ndarray (n x m x 1 x 1)
compute_force_vector
Compute the force vector due to a surface traction for a 2D element using Gaussian quadrature, where , , and are evaluated at the element’s integration points along the traction surface
Input
ip_grid: ndarray (num_pts x num_pts x 2 x 1)
w_ij: ndarray (num_pts x num_pts x 1 x 1)
face: str (+x, -x, +y, -y)
thickness: float
funcs: ndarray of Callable (2 x 1)
coeff: ndarray (2 x ncoeff)
elem: mfe.baseclasses.Element2D
Output
ndarray (n x m x 2*nnodes x 1)

## Slide 12
Bubble charts
HW5
compute_fs
Input
funcs: ndarray of Callable (2 x 1)
coeff: ndarray (2 x ncoeff)
grid: ndarray (2 x 1)
Output
ndarray (n x m x 2 x 1)
compute_J_det_surf
Input
J: ndarray (n x m x 4 x 4)
grid_shape: ndarray (n x m x 2 x 1)
face: str (+x, -x, +y, -y)
Output
ndarray (n x m x 1 x 1)
compute_force_vector
Input
ip_grid: ndarray (num_pts x num_pts x 2 x 1)
w_ij: ndarray (num_pts x num_pts x 1 x 1)
face: str (+x, -x, +y, -y)
thickness: float
funcs: ndarray of Callable (2 x 1)
coeff: ndarray (2 x ncoeff)
elem: mfe.baseclasses.Element2D
Output
ndarray (n x m x 2*nnodes x 1)
load face
function callables
function coefficients
Instance: Element2D class
load face
grid shape
function callables
function coefficients
-grid